HPC Challenge Award Class 2 Quick Reference

Note: this document is a summary and is not a substitute for reading the material provided in the references

| Benchmark | Global HPL | Global RandomAccess | Global STREAM (triad) | Global FFT |
| --- | --- | --- | --- | --- |
| Description | Solve linear system Ax = b using LU factorization with partial pivoting | Randomly update a large 1D Table | Scale and add two vectors: a ( b + a c | Complex-to-complex 1D Fast Fourier Transform (FFT): Z ( FFT(z) |
| Data Size | A is a nxn double precision matrix. b is n element vector. size(A) = 8n2 bytes > 1/2 system memory. | Table is a m element vector of unsigned 64 bit integers. size(Table) = 8m bytes > ¼ system memory | a, b and c are double precision vectors. size(a) + size(b) + size(c) = 24m bytes > ¼ system memory | Z and z are m element double precision complex vectors. size(z+Z) = 32m bytes > ¼ system memory. |
| Initialization | A and b should contain values produced by a reasonable pseudo-random generator with an expected mean of zero. | Table(i) = i. | b and c should contain values produced by a reasonable pseudo-random generator. | c should contain values produced by a reasonable pseudo-random generator. |
| Timed Region | Compute LU factorization with row partial pivoting: P[A,b] = [[L,U[,y] Solve the upper triangular system: U x = y | Create pseudo random unsigned integers r. Use lower bits of r to get index into Table. XOR r with contents of table: for i=0, NUPDATE-1 r = uInt64rand() index = AND(r,m-1) Table[index] = XOR(Table[index],r) end Indices may be generated in blocks no larger than 1024. Must use RandomAccess generator. | Scale and add two vectors 10 times. for j=0,NTRIAL-1 for i=0,m-1 a[i] = b[i] + a c[i] end end | Perform 1D complex-to-complex FFT Z = FFT(z) z input should be in linear “time” order. Z output should be in standard frequency order. Reordering time should be included. |
| Duration | Until operation is completed | NUPDATE = 4 m, or until run time is ¼ of Global HPL run time. | NTRIAL = 10. | Until operation is completed |
| Validation | Compute residuals and norms r =b – A x, ( = precision r0 = norm(r, Inf) r1 = r0/(( norm(a, 1) n) r2 = r0/(( norm(a, 1) norm(x, 1)) r3 = r0 / (( norm(a, Inf) norm(x, Inf) n); max(r1, r2, r3) < 16 | Reset random number generator. Repeat calculation using a method that will not create any errors. Should return Table to initial state. An error rate of 1% is allowed. | Compare result with an alternate implementation. Inspection? | Apply inverse FFT to Z and compare with input z max(¦z – IFFT(Z)¦) < 16 ( log2(m) |
| Performance | Gigaflops = 10-9 (2n3/3 + 3n2/2) / time | Giga Updates Per Second (GUPS) = 10-9 NUPDATE/ time | Gigabytes/sec = 10-9 24 NTRIAL m / time | Gigaflops = 10-9 5 m log2(m) / time |
| Reference | http://www.hpcchallenge.org/class2specs.pdf |